## Slide 1: CITY OF INVER GROVE HEIGHTS Playground Safety
8150 Barbara Avenue, Inver Grove Heights, MN 55077
651-450-2500
www.invergroveheights.org
Ethics, Excellence, Engagement

## Slide 2: American with Disabilities Act (ADA)
Inver Grove Heights covered by Title II of ADA
Obligations and compliance vary depending on installation date of equipment
Playgrounds are found in the ADA 2010 Standards for Accessible Design
Final guidelines issued by the US Access Board on October 18, 2000
Department of Justice adopted as a standard on March 15, 2012

## Slide 3: ADA 2010 Standards for Accessible Design
ADA references to ASTM
  ASTM F 1292-99 and ASTM 1292-04 for Impact Attenuation (1008.2.6.2)
  ASTM F 1951-99 for Accessibility of Surface Material (1008.2.6.1)
  ASTM F 1487-01 Safety Performance for Playgrounds (106.5 defined terms)

## Slide 4: American Society for Testing Materials (ASTM)
An international standards organization
Develops and publishes voluntary standards for a range of products, materials, and services
Standards are developed by a consensus of thousands of technical committees run by volunteers
There are more than 12,000 ASTM standards

## Slide 5: ASTM F1292
Standard specification for impact attenuation of surfacing materials within the use zone of playground equipment
Requires laboratory testing
Head Injury Criterion (HIC) – empirical measure of impact severity (score under 1000)
Gmax – measure of the maximum acceleration (shock) produced by an impact (score under 200g)
Engineered wood fiber installed in city playgrounds meet ASTM F1292

## Slide 6: ASTM F1951
Specification for determination of accessibility of surface systems under and around playground equipment
Requires laboratory testing
Engineered wood fiber installed in city playgrounds meet ASTM F1951

## Slide 7: ASTM F2075
Standard specification for engineered wood fiber for use as a playground safety surface under and around playground equipment
Engineered wood fiber installed in city playgrounds meet ASTM F2075

## Slide 8: ASTM F1487
Standard consumer safety performance specification for playground equipment for public use
City playground equipment installed in 2012 and later meet ASTM F1487

## Slide 9: ASTM F3313
Standard test method for determining impact attenuation of playground surfaces within the use zone of playground equipment as testing in the field
We have not performed tests to meet this standard

## Slide 10: ADA 1008.2.6 (Advisory)
Ground surfaces must be inspected and maintained regularly to ensure continued compliance with ASTM F1951. The type of surface material selected and play area use levels will determine the frequency of inspection and maintenance activities
City documents inspections performed (April – October)

## Slide 11: Accessibility and Safety
City playgrounds meet required ADA accessibility standards
City playgrounds are safe and accessible when they are used as they have been intended with proper adult supervision
City takes reasonable steps to provide a safe and accessible park and recreation system
City takes timely and appropriate actions when a safety issue is identified
City evaluates safety to guard against potential hazards that pose the risk of imminent danger of permanently debilitating and/or life- threatening injury

## Slide 12: QUESTIONS?
Eric Carlson – Parks & Recreation Director
ecarlson@invergroveheights.org
651.450.2587
Ethics, Excellence, Engagement